## Slide 1: HYDRAULIC SOFT ACTUATOR
- Under guidance of Sc. Shivdas Prasad

## Slide 2: Introduction:
Soft robotics has become an important area of robotics because compliant structures can deform continuously, adapt to irregular surfaces, and distribute contact forces during interaction. These properties are especially useful for handling delicate objects, operating in uncertain environments, and interacting safely with the human body, where compliance is a basic design requirement rather than an added feature.
In these systems, the actuator is central to performance because it not only produces motion but also influences the load path, deformation mode, stiffness distribution, and contact behavior of the robot.
First we discuss about Pneumatic Soft Actuator (PAM), like PAM is a soft actuator which has great potential in the field of bio-inspired robotics.
But PAM have lots of limitations such less loading capacity, losses, leakages, etc.
So for that we are going to discussed about Designing and Modeling of Hydraulic Soft Actuator.
And we have to design for 5kg of lift.

## Slide 3: Problem Statement:
To design and develop a single-degree-of-freedom robotic elbow joint using a hydraulic McKibben muscle actuator in an antagonistic biceps-triceps configuration, capable of lifting a minimum 5 kg load while providing the required joint torque, motion, and structural safety.
Objective:
To study the working principle and characteristics of hydraulic McKibben muscle actuators for robotic applications.
To design a single-DOF robotic elbow joint using a biceps-triceps type McKibben actuator arrangement for a minimum 5 kg load.
To analyze the required joint torque, actuator force, pressure, and braided sheath parameters.

## Slide 4: Literature Survey:
Previous studies on McKibben artificial muscles have mainly focused on understanding their working principle, mathematical modeling, and the influence of braid geometry on actuator performance. Analytical and experimental studies have established relationships between internal pressure, braid angle, contraction, actuator dimensions, and generated force. The literature also shows that the braided sheath plays a major role in converting radial expansion of the bladder into axial contraction. Finite Element Analysis has therefore been widely used to study deformation, stress distribution, and the effect of braid angle before fabrication.
Further studies have focused on improving the design and functionality of McKibben actuators. FEM-based investigations have been used for design optimization, while analytical models have been developed for predicting force and pressure-contraction behavior. Researchers have also investigated multifunctional braided muscles capable of bidirectional motion and variable stiffness. These studies demonstrate that actuator geometry, braid configuration, and material properties strongly influence the final performance of the muscle.

## Slide 5: Literature Survey:
For high-force applications, hydraulic actuation has also been investigated as an alternative to conventional pneumatic McKibben muscles. The hydraulic McKibben study by Iwata et al. demonstrated operation at pressures up to 7 MPa and investigated the design and fabrication of the braided muscle using FEM-based sleeve optimization. The reviewed hydraulic soft-actuator literature further identifies high force capability as an important advantage, while also highlighting challenges such as nonlinear deformation, hysteresis, leakage, and the need for systematic design methods.
Research Gap: Based on the reviewed literature, the present work focuses on applying a hydraulic McKibben muscle in a single-DOF robotic elbow joint using a biceps-triceps type arrangement, designed to lift a minimum 5 kg load. There is practical validation can also be done.

## Slide 6: Derivation For Pressure and Force Relation:
In a first approach toward the model of a McKibben type PAM, losses are not considered and thus, the gas enters the PAM and expands, generating a traction force and a work. To generate the volume increase, the gas performs a work input (Win) that can be described.
    dWin = ∫(P − Pex )dli.dSi
    = (P − Pex) ∫dli.dSi
    dWin = P’dV
    Where, Pex = External Force,
      P = Absolute Pressure
      P’ = Relative Pressure

## Slide 7: Derivation For Pressure and Force Relation:
As the pressure performs work by volume expansion and it is assumed that the system has no loss, all the work is converted into traction and can be expressed by Wout,
dWout = -FdL
    Where, F is the axial tension and dL is the displacement.
    The Conservation of Energy gives:
    dWin = dWout
    P’dV = -FdL
    F = - (P’ dV)/dL ........................ (1)
With the strength defined in terms of the volume change, just missing define the volume variation permitted by the mesh. The variation stops when volume reaches its maximum. At this moment, the muscle reaches the largest contraction.

## Slide 8: Derivation For Pressure and Force Relation:
Observing Fig.3, it is possible to make the length (L) and diameter (D) as a function of the angle (θ). This angle is one formed between the mesh and the axial length of the muscle. The length of fiber can be named b and n is the number of turns of the fiber around the muscle. Using b and n, it is possible to set the length and the diameter of the muscle.
    cos = (L/b)
    L = b cos …………………………… (2)
    sin = (nD)/b
    D = (b sin)/n ………………………. (3)
Making the Volume equation as function of the diameter and D & length L.
  By substituting D & L in eq 4
  We get,
  ……... (5)

## Slide 9: Derivation For Pressure and Force Relation:
By substituting the value of D & trigonometric relation in eq 8
……………….. (9)
Adopting contraction (ε) and applying Eq.9, it is possible to reach to required formulation (Daerden and Lefeber, 2000).
D = b*sin/(*n) …………… (After applying pressure)
D0 = b*sin0/(*n) ………...... (Before applying pressure)
D = D0 ………. Basic Interpretation
So, we can replace D & sin with D0 & sin0,
    cos = (L/b)
    L = b cos
    L0 = b cos0
Diff. eq (2) & eq (5) w. r. t. 
……..……………….(6)
……(7)
Substitute the value of eq (6) & eq (7) in eq (1)
After substituting and rearranging, we get:
…………….. (8)
D = b* sin /(*n)
D / sin = b /(*n)
sin^2() + sin^2() = 1